## Slide 1
Radio
By AEnI/GF/3
Johnson Lo

## Slide 2
1.RF theory
2. Antenna
3. RF measurement
4. Radio System
5. Current Development
6. Training Trend

## Slide 3
RF Theory
Radio Frequency (RF)
Radio wave is kind of Electromagnetic wave
Different wavelength/frequency have
different usage

## Slide 4
Band designation | Frequency range | Explanation of meaning of letters
HF | 0.003 to 0.03 GHz | High frequency
VHF | 0.03 to 0.3 GHz | Very high frequency
UHF | 0.3 to 1 GHz | Ultra-high frequency
L | 1 to 2 GHz | Long wave
S | 2 to 4 GHz | Short wave
C | 4 to 8 GHz | Compromise between S and X
X | 8 to 12 GHz | Used in World War II for fire control, X for cross (as in crosshair). Exotic.
Ku | 12 to 18 GHz | Kurz-under
K | 18 to 27 GHz | German: Kurz (short)
Ka | 27 to 40 GHz | Kurz-above
V | 40 to 75 GHz | 
W | 75 to 110 GHz | W follows V in the alphabet[
mm or G | 110 to 300 GHz[ | Millimeter[
RF Theory
Frequency bands
Band name | Abbreviation | Frequency and wavelength
Extremely low frequency | ELF | 3–30 Hz
 |  | 100,000–10,000 km
Super low frequency | SLF | 30–300 Hz
 |  | 10,000–1,000 km
Ultra low frequency | ULF | 300–3,000 Hz
 |  | 1,000–100 km
Very low frequency | VLF | 3–30 kHz
 |  | 100–10 km
Low frequency | LF | 30–300 kHz
 |  | 10–1 km
Medium frequency | MF | 300–3,000 kHz
 |  | 1,000–100 m
High frequency | HF | 3–30 MHz
 |  | 100–10 m
Very high frequency | VHF | 30–300 MHz
 |  | 10–1 m
Ultra high frequency | UHF | 300–3,000 MHz
 |  | 100–10 cm
Super high frequency | SHF | 3–30 GHz
 |  | 10–1 cm
Extremely high frequency | EHF | 30–300 GHz
 |  | 10–1 mm
Terahertz or tremendously high frequency | THF | 300–3,000 GHz
 |  | 1–0.1 mm
ITU bands
IEEE bands

## Slide 5
RF Theory
Hong Kong Frequency Allocation

## Slide 6
RF Theory
Modulation (Analogues and Digital)
Digital Mobile Radio:
  Project 25 a.k.a. "P25" or "APCO-25"
  TETRA (trunking)
  TETRAPOL
  NXDN/dPMR
  DMR
  D-STAR
  …
Analogues Mobile Radio (Voice):
  AM
  SSB
  FM
  PM
  …
Analogues Mobile Radio (Data):
  ASK
  FSK
    BFSK
    GFSK
  PSK
  …

## Slide 7
RF Theory
Modulation (Analogues)

## Slide 8
RF Theory
Fourier Transform
Fourier Transform pair
(synthesis)
(analysis)
Convolution in the time domain:
Multiplication in the time domain:

## Slide 9
RF Theory
Modulation (AM)

## Slide 10
Assumptions:
 = 0 (for now),
Local oscillator is synchronized with the carrier.
In practice, synchronization is achieved using a phase-locked loop (PLL).
RF Theory
Demodulation (AM)

## Slide 11
Since x(t) and y(t) are real, from conjugate symmetry, both lower sideband (LSB) and upper sideband (USB) signals carry exactly the same information.
Double-sideband (DSB) occupies 2M bandwidth in  > 0, even though all the information is contained in M.
Single-sideband (SSB) occupies M bandwidth in  > 0.
Of course, SSB requires slightly more complicated hardware, so it was originally only used in applications where bandwidth was very limited (e.g., transcontinental telephone lines).
.
RF Theory
Modulation (SSB)

## Slide 12
RF Theory
Demodulation (SSB)

## Slide 13
RF Theory
Modulation (FM)
y(t) = cos(ωct + mx(t)) = cos(ωct + m sin(ωmt)) = cos(ωct) cos(m sin(ωmt))) − sin(ωct)sin(m sin(ωmt)))
Fourier transform of first part.
x(t) = sin(ωmt) y(t) = cos(ωct + mx(t)) = cos(ωct + m sin(ωmt)) = cos(ωct) cos(m sin(ωmt))) − sin(ωct)sin(m sin(ωmt)))
|Ya(jω)|
ωc
ωc
100ωm
m = 50
|Yb(jω)|
ωc
ωc
100ωm
m = 50
Fourier transform of second part.
x(t) = sin(ωmt) y(t) = cos(ωct + mx(t)) = cos(ωct + msin(ωmt)) = cos(ωct) cos(msin(ωmt)))−sin(ωct) sin(msin(ωmt)))
Fourier transform.
x(t) = sin(ωmt) y(t) = cos(ωct + mx(t)) = cos(ωct + msin(ωmt)) =
cos(ωct) cos(msin(ωmt)))−sin(ωct) sin(msin(ωmt)))
|Y (jω)|
ωc
ωc
100ωm
m = 50

## Slide 14
RF Theory
Bandwidth (Analogues)
Name | Peak Frequency Deviation | Bandwidth | Channel Spacing
Narrowband | 2.5 kHz | 11 to 12.5 kHz | 12.5 kHz
Wideband (US Amateur Standard) | 5.0 kHz | 13 to 16 kHz | 15 to 25 kHz
FM Broadcast | 75 kHz | 180 to 200 kHz | 200 kHz
Extended SSB modes | Bandwidth | Frequency response
eSSB (Narrow-1a) | 3 kHz | 100 Hz ~ 3.10 kHz
eSSB (Narrow-1b) | 3 kHz | 50 Hz ~ 3.05 kHz
eSSB (Narrow-2) | 3.5 kHz | 50 Hz ~ 3.55 kHz
eSSB (Medium-1) | 4 kHz | 50 Hz ~ 4.05 kHz
eSSB (Medium-2) | 4.5 kHz | 50 Hz ~ 4.55 kHz
eSSB (Wide-1) | 5 kHz | 50 Hz ~ 5.05 kHz
eSSB (Wide-2) | 6 kHz | 50 Hz ~ 6.05 kHz

## Slide 15
Antenna
Types of antenna

## Slide 16
Antenna
Dipole

## Slide 17
Antenna
Radiation Pattern

## Slide 18
Antenna
Monopole

## Slide 19
Antenna
Radiation Pattern

## Slide 20
Antenna
Reception simulation

## Slide 21
Antenna
HF converage

## Slide 22
Antenna
HF signal strength
S-reading | HF |  | Signal Generator emf
 | μV (rms, Relative to 50Ω) | dBm | dB above 1uV
S9+10 dB | 160.0 | -63 | 44
S9 | 50.2 | -73 | 34
S8 | 25.1 | -79 | 28
S7 | 12.6 | -85 | 22
S6 | 6.3 | -91 | 16
S5 | 3.2 | -97 | 10
S4 | 1.6 | -103 | 4
S3 | 0.8 | -109 | -2
S2 | 0.4 | -115 | -8
S1 | 0.2 | -121 | -14

## Slide 23
RF measurement
Measuring Equipment (Comm set)

## Slide 24
RF measurement
Power Meter (existing)

## Slide 25
RF measurement
Power Meter (proposed)

## Slide 26
RF measurement
Convertor for different connectors

## Slide 27
RF measurement
RF connector type
Type N
UHF (PL259)
TNC
Reverse Polarity TNC (RPTCN)
BNC
SMA
Reverse Polarity SMA (RPSMA)

## Slide 28
RF measurement
Parameters of RF measurement
VSWR
Transmission Power
SNR
ACPR

## Slide 29
RF measurement
Measurement of SSB device

## Slide 30
RF measurement
Different Mode of SSD device
Mode | Description
USB | USB voice: Standard voice grade IF filter and voice AGC time constants
LSB | LSB voice: Standard voice grade IF filter and voice AGC time constants
USB DATA | FSK AGC time constants, optional USB wideband data filter, 300-3000 Hz BW
LSB DATA | FSK AGC time constants, optional LSB wideband data filter, 300-3000 Hz BW
USB AME | Same as USB mode with addition of the carrier in transmit mode at a level of -6 dB relative to PEP
LSB AME | Same as LSB mode with addition of the carrier in transmit mode at a level of -6 dB relative to PEP
USB PCS | Same as USB mode with addition of the carrier in transmit mode at a level of -16 dB relative to PEP

## Slide 31
Radio System
Radio System of GFS

## Slide 32
Radio System
Radio System of GFS

## Slide 33
Radio System
Radio System of GFS

## Slide 34
Radio System
Radio Channels of GFS
GFS - Channels of the Existing Radio ACOM Console System |  | 
Channels |  | Remarks
Radio 1 | TC 131.3 | 
Radio 2 | HQ 131.2 | Maintenance by EMSD
Radio 3 | HQ 132.2 | Maintenance by EMSD
Radio 4 | Police (TRS) | 
Radio 5 | SUS 131.2 | 
Radio 6 | Hill 275 131.2 | 
Radio 7 | HQ 48.2 | Maintenance by EMSD
Radio 8 | TMS 48.2 | 
Radio 9 | APRON | Maintenance by EMSD
Radio 10 | UHF HQ | Maintenance by EMSD
Radio 11 | TMS 132.2 | 
Radio 12 | HF #1 | Maintenance by EMSD
Radio 13 | HF #2 | Maintenance by EMSD
Radio 14 | Pol Tetra | 
Radio 15 | Police CC3 | 

## Slide 35
Radio System
Radio of GFS
AM Modulation
50W
131.3MHz, 131.2MHz, 132.2MHz
AM Modulation
100W
277.1MHz
FM Modulation
30W
403 to 470MHz
Old Motorola MTR2000 was replace by XiR M6660
FM Modulation
100W
48.2MHz
AM SSB Modulation
1000W
2MHz to 25MHz
SELCAL Coder (Selective calling), Generated by ACOM

## Slide 36
Radio System
New ACCC system of GFS

## Slide 37
Radio System
New ACCC system of GFS

## Slide 38
Radio System
New ACCC system control panel

## Slide 39
Radio System
Problems of New ACCC System of GFS

## Slide 40
Current Development
SDR
Software-Defined Radio
A software-defined radio (SDR) system is a radio communication system which uses software for the modulation and demodulation of radio signals.

## Slide 41
Current Development
Different between Radio and SDR

## Slide 42
Current Development
Normal components

## Slide 43
Current Development
Software Interface

## Slide 44
Current Development
General Setup

## Slide 45
Current Development
Decoding Digital Radio
Decoding Digital Voice (P25, DMR, NXDN, D-STAR)
A program called “digital speech decoder” (DSD) can be used as a radio scanner to easily and cheaply listen to unencrypted digital radio voice conversations.

## Slide 46
Current Development
DSD interface

## Slide 47
Current Development
Virtual Audio Cable (VAC

## Slide 48
Training Trend
Different types of programming tools

## Slide 49
Training Trend
Interface with USRP

## Slide 50
Training Trend
Program interface

## Slide 51
Training Trend
Spectrum and waterfall diagram

## Slide 52
Training Trend
QPSK

## Slide 53
Training Trend
SSB simulation

## Slide 54
Training Trend
End of Presentation
Thank you
Question?